## Slide 1
TRAINING @ FORREST.ONE
SESSION 2 OF 12
Network Fundamentals + CompTIA Security+ SY0-701
Switching, VLANs & Network Architectures
Devices, routes and segments: how switches and routers move traffic, how routing protocols and address translation choose paths, how VLANs, trunks and spanning tree segment a campus, and how wireless and physical design decide what an attacker can reach.
NETWORK
SWITCHING
ROUTING
VLANS
© Billy Forrest

## Slide 2
SESSION OBJECTIVES
By the end of this session you will be able to
Compare switching with routing frames by MAC address against packets by IP address
Describe the security appliances firewalls, intrusion detection and intrusion prevention
Explain the traffic shapers load balancers, forward proxies and reverse proxies
Compare the storage models network attached storage against a storage area network
Define the cloud terms and models virtualisation, private networks, security groups, gateways
Compare the routing protocols static, distance vector, link state and path vector
Explain route selection administrative distance, then the metric, then the longest match
Describe translation and redundancy NAT, PAT, first hop redundancy, VLANs and trunks
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
2

## Slide 3
CHAPTER 1 · INFRASTRUCTURE DEVICES
Network Infrastructure Devices
Switches and routers layer 2 frame forwarding against layer 3 path selection
Security appliances firewalls, intrusion detection and intrusion prevention
Traffic shaping devices load balancers, forward proxies and reverse proxies
Storage and wireless network attached storage, storage area networks, access points
Cloud networking virtualised network functions, private clouds, service models
The thread
Every device is also a security boundary. Ask of each one, who does this protect, and from whom? Detection alone is not defence.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
3

## Slide 4
CHAPTER 1 · INFRASTRUCTURE DEVICES
Switches forward frames, routers forward packets
Switch a layer 2 device, forwarding frames by MAC address
MAC address 48 bits as six hex pairs; the first three octets are the OUI
Learning the table is built from the source address on every arriving frame
Scope a switching decision stays inside one network or broadcast domain
Router a layer 3 device, forwarding packets by IP address between networks
Routing table a next hop per destination, learned by protocols such as OSPF and BGP
The distinction that matters
Switching is local and joins devices; routing joins networks. A capture shows the hardware addresses of the devices that spoke on that segment, even when the traffic later crossed a router.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
4

## Slide 5
CHAPTER 1 · INFRASTRUCTURE DEVICES
The switch forwarding table
1
Learn
record the source MAC and the port it arrived on
2
Look up
find the destination MAC in the table
3
Forward
out of the one port that holds the destination
4
Flood
unknown unicast goes to every port but the source
5
Broadcast
always flooded, which is why a loop is fatal
MAC flooding
Fill the table with bogus source addresses and the switch degrades to hub mode, so every frame becomes visible to the attacker. That is why port security limits how many addresses may appear on one port.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
5

## Slide 6
CHAPTER 1 · INFRASTRUCTURE DEVICES
Security appliances: detect, prevent, filter
Firewall filters on rules built from addresses, ports, protocols and content
Placement at the perimeter, and internally between zones
Intrusion detection monitors passively and raises an alert, but never blocks
Intrusion prevention sits inline and can drop the packet or reset the connection
Sensors a network sensor watches a segment; a host sensor watches one machine
Defence in depth all three layers together, because one will be bypassed
Say it plainly
The firewall refuses by rule, detection reports after the fact, and prevention stops it in line. An alert with nobody watching it is not a control.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
6

## Slide 7
CHAPTER 1 · INFRASTRUCTURE DEVICES
Load balancers and proxies
Load balancer spreads requests across a pool so no server is overwhelmed
Round robin each request goes to the next server in turn
Least connections each request goes to the server with the fewest active sessions
Forward proxy sits in front of the clients, hides them and filters outbound requests
Reverse proxy sits in front of the servers, caches content and terminates TLS
Availability one failed server no longer takes the service down
Which side is protected
A forward proxy protects the client side of the conversation and a reverse proxy protects the server side. Both hide one side from the other.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
7

## Slide 8
CHAPTER 1 · INFRASTRUCTURE DEVICES
Storage and wireless hardware
Device | Role | Protocol or standard
Network attached storage | File level sharing over the network | NFS and SMB
Storage area network | Block level storage for servers | Fibre Channel
Access point | Bridges wireless clients onto the wired network | 802.11ac and 802.11ax
Wireless controller | Configures many access points centrally | One policy interface
Wireless bridge | Joins two segments with no cable | Point to point
Pairing rule
NAS is file level over the network with NFS and SMB; a SAN is block level with Fibre Channel and looks to the server like a local disk. Learn the pairings, because the exam asks which one a server actually needs.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
8

## Slide 9
DISCUSSION
A firewall, an intrusion detection system and an intrusion prevention system all see the same traffic. Which one stops an attack, and why can you not rely on it alone?
Prevention blocks inline, detection only reports, and the firewall refuses by rule. Defence in depth assumes one of the three will be bypassed or misconfigured.
An IPS is only as good as its signatures and its tuning; a firewall rule set is only as good as its last review. Ask the room who actually reads the alerts.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
9

## Slide 10
CHAPTER 2 · CLOUD & ROUTING
Cloud Networking and Routing Foundations
Cloud computing replaces dedicated appliances with software, and moves the boundary
Routing begins with a static route typed by hand
Then a dynamic protocol that learns the topology for itself
The question to keep asking what breaks if this mechanism is misconfigured?
The thread continues
Watch where the attack surface sits, because it moves with every design choice. Virtual appliances put the management plane and the hypervisor in the attacker's sights, and every routing option decides who reaches what.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
10

## Slide 11
CHAPTER 2 · CLOUD & ROUTING
Network functions virtualisation
Virtualisation firewalls, routers and load balancers become software
Platform they run on ordinary servers or virtual machines
Benefits lower cost, faster deployment and easy scaling
Speed a virtual firewall deploys in a moment, not after a procurement cycle
New targets the management plane and the hypervisor
The trade the same function, but the security boundary has moved
What moved
The appliance left the rack, so the patch cycle, the console access and the configuration file are now software problems that somebody must own.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
11

## Slide 12
CHAPTER 2 · CLOUD & ROUTING
Private clouds, security groups and gateways
Virtual private cloud a logically isolated network inside a public cloud
You define the address ranges, the subnets and the route tables
Security groups stateful firewalls on a resource, so replies are allowed automatically
Network ACLs instead filter at the subnet boundary
VPN gateway an encrypted tunnel back to the office
Direct connection private, and avoids the public internet entirely
Design rule
Default to deny, then open only what the service actually needs. Every open rule is a decision somebody will have to justify later.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
12

## Slide 13
CHAPTER 2 · CLOUD & ROUTING
Deployment and service models
Model | Who manages what | Typical use
Public cloud | Provider owns the infrastructure | Scale, pay as you go
Private cloud | One organisation, on site or hosted | Strict compliance needs
Hybrid cloud | Sensitive data private, the rest public | Control with lower cost
Software as a service | Provider runs the whole application | Mail and office suites
Infrastructure as a service | You run operating systems and data | Rented compute and storage
Platform as a service | You build only the application | Application development
Where the responsibility stops
Service models shift the boundary of responsibility, never the whole of it. On software as a service you still manage your data and your users; on infrastructure as a service you also patch the operating system.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
13

## Slide 14
CHAPTER 2 · CLOUD & ROUTING
Static routing
Static route typed by an administrator and never changed on its own
Good for small networks, stub networks and default routes
Stub network one way in and one way out
Default route catches every destination the table does not list
Administrative distance 1, so it is trusted above anything learned dynamically
The cost it does not adapt, so a failed link stays in the table
Predictable, until it is not
A static route gives control and no surprises until the topology moves, and then traffic is sent into a dead end that the table still believes in.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
14

## Slide 15
CHAPTER 2 · CLOUD & ROUTING
Dynamic routing and distance vector
Dynamic protocol learns by exchanging information with its neighbours
Distance vector a router advertises its whole table: routing by rumour
RIP Routing Information Protocol measures a path in hop count
The limits 15 hops is the maximum usable count, and 16 means unreachable
Convergence slow convergence brings routing loops and black holes
Defences split horizon, route poisoning and hold down timers
Why 16 exists
The hop limit is how RIP stops a route circling for ever. Neighbours share what they know until the network converges, and while they disagree, traffic disappears.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
15

## Slide 16
CHAPTER 2 · CLOUD & ROUTING
Open Shortest Path First
OSPF the open standard link state protocol
Link state advertisement each router describes its own links to every other router
Link state database every router holds the same one, so the same map of the network
Shortest path first each router runs the calculation with itself as the root
Cost follows bandwidth, so a lower cost is the preferred link
Areas area 0 is the backbone, and every other area attaches to it
The link state idea
Distance vector routers trust rumour; link state routers each hold the whole map and then work out their own best path from it.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
16

## Slide 17
CHAPTER 3 · ROUTE SELECTION & TRANSLATION
Route Selection, Translation and Inter-VLAN Routing
Choosing administrative distance ranks the source a route came from
Translating we rewrite the addresses themselves as traffic crosses a boundary
Protecting first hop redundancy makes the default gateway survive a failure
Carrying one physical link carries every VLAN: router on a stick
Why this chapter exists
Each of these is a control you may be asked to justify, and each fails in a way that looks like something else at first. Misconfiguration here is one of the most common causes of a real outage.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
17

## Slide 18
CHAPTER 3 · ROUTE SELECTION & TRANSLATION
EIGRP and BGP
EIGRP advanced distance vector, and Cisco proprietary in origin
Feasible successor the diffusing update algorithm keeps a backup path ready
Recovery failover to that backup needs no recalculation of the network
Metrics bandwidth, delay, load and reliability, not hop count alone
BGP the path vector protocol of the internet
Selection attributes and policy, such as the autonomous system path length
Two worlds
EIGRP is fast inside the enterprise; BGP carries the internet and is the protocol behind route hijacks. Both must be secured and monitored.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
18

## Slide 19
CHAPTER 3 · ROUTE SELECTION & TRANSLATION
Administrative distance decides, then the metric
Route source | Administrative distance | Trust
Connected route | 0 | Highest
Static route | 1 | Very high
EIGRP | 90 | High
OSPF | 110 | Medium
RIP | 120 | Low
Distances first, then the metric
A router often learns the same destination from more than one source, and administrative distance settles the argument because the lowest value wins. Once the source is chosen, its metrics pick between paths, and the longest match rule means the most specific route wins overall.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
19

## Slide 20
CHAPTER 3 · ROUTE SELECTION & TRANSLATION
Network address translation
NAT rewrites addresses in the packet header as traffic crosses a boundary
Reason one to slow the exhaustion of the IPv4 address pool
Reason two to hide the internal layout from the outside
Static NAT one private address to one public address, for a published server
Dynamic NAT an address taken from a pool, first come first served
Vocabulary inside and outside give position; local and global give scope
Log the translations
A translation table is evidence and a troubleshooting tool at the same time. Without it, an outbound connection cannot be traced back to a workstation.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
20

## Slide 21
CHAPTER 3 · ROUTE SELECTION & TRANSLATION
Port address translation
PAT maps many private addresses onto one public address
The trick every session is given a unique port number
Translation table tracks every active connection
The result two hosts appear as one public address on two different ports
Inbound services need a port forwarding rule, because the router cannot know who asked
In the wild most home routers run PAT by default
The everyday form
Port address translation is the version of NAT that hides a whole office behind a single public address, told apart by port number alone.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
21

## Slide 22
CHAPTER 3 · ROUTE SELECTION & TRANSLATION
First hop redundancy protocols
The problem if the default gateway dies, everything behind it loses the outside world
The fix a shared virtual IP address that floats between routers
HSRP Hot Standby Router Protocol keeps one active router and one standby
VRRP the open standard version, with a master and several backups
GLBP goes further and shares the forwarding load between routers
Preemption hands the role back to the best router
Transparent failover
Clients never learn that the gateway changed underneath them, because the address they were configured with is still answering. Test the failover before you need it.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
22

## Slide 23
CHAPTER 3 · ROUTE SELECTION & TRANSLATION
Subinterfaces and router on a stick
Subinterface a logical interface built on one physical router port
Each one serves a single VLAN
The design the router reaches every VLAN over one shared trunk
Tagging each subinterface carries the 802.1Q tag for its own VLAN
Result the router routes between the VLANs and each gets a gateway address
The cost all VLANs share one physical link, so it can become the bottleneck
One link, several gateways
Router on a stick is cheap and easy to draw, and it puts every VLAN on one conversation. A busy campus will feel that link.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
23

## Slide 24
BREAK
10 MINUTES
Back soon: VLANs, trunking, spanning tree, wireless deployment and the room itself.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
24

## Slide 25
CHAPTER 4 · VLANS & SPANNING TREE
VLANs, Switching and Spanning Tree
VLANs split one switch into logical broadcast domains, the core containment control
Trunks and tags how many VLANs cross one link, and how they stay apart
Port security and the guard features that protect an access port
Spanning tree one loop free path, with redundancy held in reserve
Frames why the maximum size breaks networks quietly when it is wrong
Why these five
Every mechanism in this chapter exists for availability or for containment, and every one of them fails in a way that looks like something else at first. That is what makes this chapter worth your attention.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
25

## Slide 26
CHAPTER 4 · VLANS & SPANNING TREE
VLAN fundamentals
VLAN a logical broadcast domain built inside the switching hardware
Without one every device on the switch hears every broadcast
Membership by port, by hardware address or by protocol
VLAN 1 the default; the native VLAN is the one carrying untagged frames
Management VLAN keeps administration traffic away from users
The payoff fewer broadcasts, a smaller blast radius, no easy lateral movement
Segmentation is a control
A guest VLAN keeps visitors away from internal resources, and naming your VLANs properly makes the design document itself.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
26

## Slide 27
CHAPTER 4 · VLANS & SPANNING TREE
Trunking and tagging
Trunk port carries many VLANs between switches
802.1Q inserts a four byte tag into the Ethernet frame
The VID 12 bits, giving just over four thousand usable VLANs
Receiving switch reads the tag and keeps the traffic in the right VLAN
Native VLAN crosses the trunk untagged, so a mismatch can leak between VLANs
Access port carries a single VLAN to one endpoint
VLAN hopping
Two methods: switch spoofing, where the attacker negotiates a trunk, and double tagging, where the native VLAN is spoofed. Tag every trunk consistently and treat an access port as access only.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
27

## Slide 28
CHAPTER 4 · VLANS & SPANNING TREE
A practical VLAN design
VLAN | Name | Purpose
10 | MANAGEMENT | Switch and infrastructure administration
20 | SERVERS | Internal servers, never user traffic
30 | WORKSTATIONS | User workstations
40 | DMZ | Public facing services
999 | BLACKHOLE | Unused quarantine VLAN for dead ports
Key rule
VLAN 1 is the default native VLAN and a known attack surface. Move it to an unused ID, prune unused VLANs from every trunk, and set trunks to explicit allowed lists. That is what blunts VLAN hopping, where an attacker spoofs a trunk or double tags a frame on the native VLAN to jump segments.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
28

## Slide 29
CHAPTER 4 · VLANS & SPANNING TREE
Switch interface configuration
Speed and duplex must agree at both ends of a link
A mismatch brings collisions and very poor throughput
Port security limits how many hardware addresses may appear on a port
Violations can drop the traffic, log it, or shut the port down
PortFast skips the listening states on a port that leads to one endpoint
BPDU Guard shuts a port that receives a bridge protocol data unit
The quiet access port
A port that leads to one workstation should never speak spanning tree. BPDU Guard is how you find out that somebody plugged a switch into it.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
29

## Slide 30
CHAPTER 4 · VLANS & SPANNING TREE
Loops and the root bridge
Redundancy two links between switches create a layer 2 loop
Broadcast storm frames circulate, and the network is consumed in seconds
The MAC table destabilises as one address appears on two ports
STP builds one loop free logical topology by blocking redundant ports
Root bridge the lowest bridge identifier wins: priority plus MAC address
Root port each switch picks its best port toward the root; the rest block
One logical path
One logical path, no loops, with the redundant link held in reserve until the forwarding path fails.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
30

## Slide 31
CHAPTER 4 · VLANS & SPANNING TREE
STP port states and convergence
State | Forwards? | Role
Blocking | No | Listens for BPDUs only, holds the link in reserve
Listening | No | Transitional, still learning the topology
Learning | No | Builds the MAC table but forwards nothing
Forwarding | Yes | Normal operation
Disabled | No | Administratively down
Convergence
Blocking, listening and learning all mean no data. Traditional STP takes thirty to fifty seconds to converge after a topology change; rapid spanning tree does it in seconds. Know which one your campus runs.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
31

## Slide 32
CHAPTER 4 · VLANS & SPANNING TREE
Rapid and multiple spanning tree
RSTP 802.1w converges in seconds rather than tens of seconds
New roles it adds the alternate and backup port roles
New states discarding replaces the blocking and listening states
MSTP 802.1s maps groups of VLANs to instances, so redundant links get used
Per VLAN STP instead gives every VLAN its own tree
Root placement choose the root bridge deliberately, never leave it to chance
Where you want the root
The root bridge should be the switch at the centre of your design, not the one that happened to have the lowest hardware address on the day.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
32

## Slide 33
CHAPTER 4 · VLANS & SPANNING TREE
STP attacks and the guard features
Threat | Feature | Effect
Attacker becomes the root bridge | Root Guard | Port cannot become a root port
BPDUs on an access port | BPDU Guard | Port shuts down on receipt
Rogue switch insertion | Port security | Limits the MACs allowed per port
Flooding the MAC table | Port security | Stops the switch degrading to hub mode
Why it matters
A rogue root bridge forces all traffic through the attacker's switch, which is invisible interception rather than an outage. Root Guard and BPDU Guard are the two lines of defence, and port security blunts MAC flooding at the same time.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
33

## Slide 34
DISCUSSION
Two switches, equal priority. Which becomes root, and what converges?
The tiebreaker is the MAC address: the lower one wins. Then each non-root switch picks its root port by path cost to the root.
The gigabit link at cost four forwards and the hundred megabit link at cost nineteen blocks. If the gigabit link fails, the blocked port transitions and the network reconverges: seconds on RSTP, thirty to fifty seconds on classic STP.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
34

## Slide 35
CHAPTER 4 · VLANS & SPANNING TREE
Maximum transmission unit and jumbo frames
Standard MTU 1500 bytes for Ethernet
Larger packet must be fragmented, or dropped if fragmentation is refused
The signal an ICMP message returns to the sender when a fragment is refused
Jumbo frames raise the limit to about 9000 bytes
Why bother they cut header overhead in data centres and storage networks
The trap every device in the path must agree, or packets simply vanish
A quiet failure
An MTU mismatch is a classic cause of strange, partial failures: small requests that work, large transfers that stall, and no obvious error anywhere.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
35

## Slide 36
QUIZ
Activity: design the segmentation
Which VLAN should host the web server facing the internet?
Which VLAN should never carry user traffic?
Why isolate management traffic from workstations?
What risk does the default native VLAN create?
Name two attacks VLAN segmentation prevents.
The DMZ hosts public services, the blackhole swallows unused access ports, and management should never share a domain with users. Think microsegmentation: isolate the sensitive workloads, not just whole departments.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
36

## Slide 37
SESSION 2 · SEGMENTATION & ZONES
From segments to security zones
Segmentation VLANs and subnets become security zones
DMZ public facing services, isolated from the internal network
DMZ firewalls an external and an internal firewall, often with a proxy between
Blast radius a compromise stays inside its own segment
Lateral movement zones block east-west spread across the campus
Campus and IoT access connects, distribution enforces policy, unmanaged devices isolated
The exam line
Architecture is a control, not plumbing. When a question asks how to contain a breach, the answer is nearly always segmentation.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
37

## Slide 38
CHAPTER 5 · WIRELESS & PHYSICAL
Wireless and Physical Deployment
Frequencies the bands and channel widths, and what each one is good for
Names and modes the identifiers a wireless network uses
Encryption a history of what happens when a control is broken early
Authentication enterprise sign in, and guest design
The room the rack, the cable and the physical access
The principle returns
Notice how often the same idea comes back: separate what must not touch. And notice how often physical access decides the final outcome.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
38

## Slide 39
CHAPTER 5 · WIRELESS & PHYSICAL
Channels and frequencies
2.4 GHz eleven channels, and only 1, 6 and 11 do not overlap
5 GHz up to twenty three non overlapping channels, so busy offices prefer it
6 GHz used by Wi-Fi 6E, and adds far more spectrum again
Lower frequencies travel further and pass through walls better
Higher frequencies carry more data over shorter distances
Channel width wider channels raise throughput and consume the space around them
Choose for the job
Pick the band for the requirement, not for the marketing number. Twenty megahertz is the steady default, and adjacent access points must not overlap.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
39

## Slide 40
CHAPTER 5 · WIRELESS & PHYSICAL
Network names and modes
SSID the service set identifier, the network name clients see
Infrastructure mode sends all traffic through an access point
Ad hoc mode devices talk directly, with weaker security and no central control
BSSID the basic service set identifier names a single access point
ESSID the extended service set identifier lets clients roam between access points
Hiding the name stops nothing; client isolation keeps users apart
Roaming
Roaming needs one shared name and separate radios behind it, with the controller setting power and channel so the client moves when it should.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
40

## Slide 41
CHAPTER 5 · WIRELESS & PHYSICAL
Wireless encryption
WEP wired equivalent privacy: short keys and a weak schedule, broken quickly
WPA added the temporal key integrity protocol as a stopgap
WPA2 replaced that with AES, and is still the common baseline
WPA3 adds simultaneous authentication of equals, resisting offline cracking
Personal mode one pre shared key for everybody
Enterprise mode 802.1X with a central authentication server
The rule
Retire WEP entirely. Run WPA2 or WPA3 with AES, and move to enterprise mode wherever you have an authentication server to point at.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
41

## Slide 42
CHAPTER 5 · WIRELESS & PHYSICAL
Enterprise authentication and guest networks
802.1X authenticates a device before it joins the network
Authentication server checks credentials centrally, so the access point does not decide
EAP the extensible authentication protocol carries the exchange
Protected EAP hides that exchange inside a TLS tunnel
EAP TLS uses certificates on both the client and the server
Guest network its own name, its own VLAN, a bandwidth limit and clear rules
Guests get the internet
Guests get the internet and nothing else, and they accept an acceptable use policy before they get even that. Survey before you mount.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
42

## Slide 43
CHAPTER 5 · WIRELESS & PHYSICAL
Access points and antennas
Standalone access point configured on its own, fine for a small site
Controller based managed centrally, with power and channel set for every unit
Consistency the controller keeps policy identical across the estate
Omnidirectional radiates all around, for open areas
Directional a Yagi focuses a beam for a long point to point link
Gain and survey more gain means more reach; a heat map shows real coverage
Measure, do not guess
Place access points by measurement, not by eye. A survey before installation is cheaper than a second visit after the complaints.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
43

## Slide 44
CHAPTER 5 · WIRELESS & PHYSICAL
Installation, power and environment
Rack a standard equipment rack is nineteen inches wide
Heights one rack unit is 1.75 inches of vertical space
Labelling label every cable and document the patch panel
Patch panel protects the switch ports and eases every change
Physical security lockable racks and a controlled room
Cooling and environment hot and cold aisles, a UPS, and no water, heat or dust
The bottom line
Physical access defeats every logical control you own. Label it, or you will lose it, and troubleshooting becomes guesswork.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
44

## Slide 45
QUIZ
Check your understanding
Open Quiz_Session_02.html in your browser.
20 questions, immediate feedback, and a topic tag on every question.
Read each explanation: the distractors teach as much as the answer.
Score 70% or better before you move on to Session 3.
Every question is tagged with its banked topic area, covering infrastructure devices, VLANs and trunking, spanning tree and network architectures.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
45

## Slide 46
KEY TAKEAWAYS
Switches forward frames routers forward packets.
Each appliance does one job refuse, report, block.
Cloud moves the boundary software functions, security groups.
Distance ranks the source the metric picks the path.
The longest match wins first the most specific route.
Translation conserves addresses NAT and PAT, told apart by port.
VLANs contain, trunks carry tags spanning tree keeps one path.
Wireless means WPA2 or WPA3 with AES and a guest VLAN.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
46

## Slide 47
REVISION CHECKLIST
Before next session
Retake the quiz until you score 70% or better without guessing
Redraw one design a VLAN plan, a distance table, or a wireless policy
Trace an election two switches, two links: pick the root bridge and the blocked port
Read every device twice once as plumbing, once as a boundary
Read ahead Session 3: DNS, DHCP, NTP and SSH, and how each is attacked
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
47

## Slide 48
NEXT SESSION
Session 3 · Network Services & the Attack Surface
The services every network runs, and how each one can be turned against you
DNS: hierarchy, record types, poisoning and DNSSEC
DHCP: DORA, rogue servers, starvation and snooping
NTP and SSH: time integrity, and the encrypted management channel
Every service is a service, and every service is a target
Network Fundamentals + CompTIA Security+ SY0-701 · Session 2
© Billy Forrest
48