## Slide 1
TRAINING @ FORREST.ONE
SESSION 3 OF 12
Network Fundamentals + CompTIA Security+ SY0-701
Network Services & the Attack Surface
Ports, protocols, documentation, monitoring and recovery, then the core services an attacker can reach.
NETWORK
PORTS
OPERATIONS
SERVICES
© Billy Forrest

## Slide 2
WELCOME · WHERE WE ARE
Where Session Three goes
Sessions 1 and 2 models, addressing, switching and architectures
Today the operations that keep a network running, and the services on it
Chapters 1 to 2 well-known ports, traffic types, documentation and agreements
Chapters 3 to 5 life cycle, controlled change, monitoring and resilience
Chapter 6 the core services: addressing, names, time and remote access
The foundation closes from Session 4 the Security+ core begins
The question to hold what does this service let an attacker do?
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
2

## Slide 3
SESSION OBJECTIVES
By the end of this session you will be able to
Read a port number and say what the service behind it lets an attacker do
Compare plaintext and encrypted services FTP and SFTP, Telnet and SSH, HTTP and HTTPS
Describe the traffic types unicast, broadcast, multicast and anycast
Document a network diagrams, inventories, address management and service levels
Control change life cycle, end of support, decommissioning and the change process
Monitor and recover baselines, logs, SNMP, flow data, recovery objectives and sites
Explain the core services dynamic addressing, names, time and remote access
Verify on Kali dig, ss, journalctl and log analysis
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
3

## Slide 4
CHAPTER 1 · PORTS, PROTOCOLS AND TRAFFIC TYPES
File Transfer and Remote Access
FTP port 21 to control the session, port 20 to move the data, no encryption
SFTP the same file transfer inside Secure Shell, on port 22
SSH an encrypted command line on port 22, the modern default
Telnet port 23, plaintext and legacy; avoid it
RDP port 3389, a full graphical desktop session
Rule of thumb if the name has no S, assume plaintext
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
4

## Slide 5
CHAPTER 1 · PORTS, PROTOCOLS AND TRAFFIC TYPES
Email, Web and Name Services
SMTP port 25 between servers, port 587 for client submission
DNS port 53: UDP for queries, TCP for zone transfers
DHCP server on port 67, client on port 68
HTTP port 80, stateless
HTTPS port 443, inside Transport Layer Security
Troubleshoot names first names resolve before anything else, so check port 53 early
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
5

## Slide 6
CHAPTER 1 · PORTS, PROTOCOLS AND TRAFFIC TYPES
Management and Communication Ports
Protocol | Port | Purpose
SNMP | 161 UDP | Manager polls a device
SNMP | 162 UDP | Device sends a trap
LDAP | 389 | Directory queries
LDAP over TLS | 636 | Encrypted directory queries
SIP | 5060 | Call signalling
SIP over TLS | 5061 | Encrypted call signalling
Notice the pattern: the protected form always moves to a different port. Port 389 becomes 636, and 5060 becomes 5061.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
6

## Slide 7
CHAPTER 1 · PORTS, PROTOCOLS AND TRAFFIC TYPES
How Traffic Is Addressed
Unicast one sender to one receiver, the everyday case
Broadcast one sender to every device on the segment
Contained a broadcast stays inside one subnet to limit the noise
Multicast one sender to the group that joined the stream
Anycast one sender to the nearest of many sharing one address
Why anycast matters global name servers and content networks scale on it
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
7

## Slide 8
DISCUSSION
Which service would you close first on an internet-facing router?
Telnet on port 23 and FTP on port 21 send credentials in clear text, and both have encrypted replacements already: SSH on 22 and SFTP on 22. Then ask which management ports, such as SNMP on 161 or LDAP on 389, genuinely need to be reachable from outside.
Every open port is a decision. Every service you do not need is attack surface you did not have to defend.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
8

## Slide 9
CHAPTER 2 · DOCUMENTATION, AGREEMENTS AND SURVEYS
Physical and Logical Diagrams
Diagram | Shows | Answers
Physical | Devices, ports in use, cable runs | Where the cable actually goes
Logical | Addressing, VLAN segments, traffic flow | How the traffic actually moves
One workstation drops: reach for the physical diagram and find the dead port. Everything is slow: reach for the logical diagram and find the route that is too long.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
9

## Slide 10
CHAPTER 2 · DOCUMENTATION, AGREEMENTS AND SURVEYS
Specialised Diagrams
Rack diagram the unit position of each device, and its power feeds
One rack unit 1.75 inches of vertical space
Cable map cable paths, labels and both termination points
Wiring schematic structured cabling, patch panels and distribution frames
Floor plan equipment rooms, cable tray routes and access points
Use the drawing to plan the change, not only to record it
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
10

## Slide 11
CHAPTER 2 · DOCUMENTATION, AGREEMENTS AND SURVEYS
Asset Inventory and Address Management
Asset record serial number, location, configuration and owner
Software record version, licence key and installation location
Warranties and service agreements, with their end dates
Address management tracks every static and dynamic allocation in one place
Integration address changes flow into the name system
Conflict detection finds duplicate addresses before your users do
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
11

## Slide 12
CHAPTER 2 · DOCUMENTATION, AGREEMENTS AND SURVEYS
Service Level Agreements
What it defines uptime, response time and resolution time
Each additional nine cuts permitted downtime roughly tenfold
Design consequence uptime targets drive redundancy and failover
Internal agreement between IT and other business units
External agreement with a provider, backed by service credits
The catch every clause you sign has a build cost attached
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
12

## Slide 13
CHAPTER 2 · DOCUMENTATION, AGREEMENTS AND SURVEYS
Wireless Site Surveys
Predictive survey before installation: floor plan plus modelling software
Validation survey after installation: measured signal, noise and throughput
Heat map signal strength, noise floor and channel utilisation
Lower band three non-overlapping channels: 1, 6 and 11
Higher band many more non-overlapping channels, shorter range
What the data decides access point placement and the channel plan
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
13

## Slide 14
CHAPTER 3 · LIFE-CYCLE AND CONTROLLED CHANGE
Life-Cycle and Firmware Management
End of Life the vendor stops selling the product
End of Support no more patches arrive; this is the security cliff
Unsupported equipment keeps every flaw found afterwards open
Update path download, verify the source, stage, test, deploy
Version control keeps similar devices on one version
Rollback a tested rollback plan, inside a maintenance window
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
14

## Slide 15
CHAPTER 3 · LIFE-CYCLE AND CONTROLLED CHANGE
Asset Decommissioning
Sanitise first factory reset and erase the configuration
Certificates and accounts remove certificates, delete stored credentials
Physical destruction the strongest assurance for storage media
Degaussing and overwriting for magnetic media and less sensitive data
Environmental duty certified recycling under electronic waste rules
Then the records update inventory, diagrams and monitoring
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
15

## Slide 16
CHAPTER 3 · LIFE-CYCLE AND CONTROLLED CHANGE
Controlled Change
The problem uncontrolled change is a leading cause of outage
Change Advisory Board reviews and approves anything that disrupts service
Standard change routine and pre-approved
Normal change planned, tested and reviewed
Emergency change implemented first, reviewed afterwards
Every request carries justification, risk, impact, rollback and result
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
16

## Slide 17
CHAPTER 3 · LIFE-CYCLE AND CONTROLLED CHANGE
The document you did not update is the one you will trust
Four records the network diagram, the asset inventory, the configuration baseline and the monitoring
Skip one and the next engineer works from fiction
Worse than nothing a diagram that disagrees with reality earns confidence it has not deserved
Make documentation part of the change itself, with a named owner, rather than a chore for later.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
17

## Slide 18
CHAPTER 4 · CONFIGURATION AND MONITORING TOOLS
Configuration Management and Backups
Production configuration what the device is running right now
Baseline configuration the approved template for that device type
Configuration drift slow divergence from the baseline, one tweak at a time
Compliance checking compares running settings against policy
Backup routes manual export, scheduled capture or triggered on change
Keep three copies locally, in version control and off site, then test a restore
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
18

## Slide 19
CHAPTER 4 · CONFIGURATION AND MONITORING TOOLS
Simple Network Management Protocol
The model a manager asks, an agent answers, a database holds the values
Object identifiers name each value that can be requested
GET and SET GET reads a value, SET changes one
TRAP the unsolicited alert when something crosses a threshold
Ports 161 for requests, 162 for traps
Authentication a community string is a plaintext password; use version 3
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
19

## Slide 20
CHAPTER 4 · CONFIGURATION AND MONITORING TOOLS
Flow Data
A flow record summarises a conversation, not a packet
NetFlow records collected as traffic crosses an interface
sFlow samples packets at intervals, suited to fast links
IPFIX the standard export that grew out of NetFlow version 9
What a flow holds addresses, ports, protocol, byte counts, timestamps
The advantage lower overhead and longer retention than full capture
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
20

## Slide 21
CHAPTER 4 · CONFIGURATION AND MONITORING TOOLS
Flow Records or Full Capture
Question | Flow records | Full capture
What it holds | Summary of a conversation | Every byte of every packet
Cost | Low storage, long retention | High storage, short retention
Best for | Trends, capacity, floods | Protocol faults, malware detail
Tools | NetFlow, sFlow, IPFIX | Wireshark, tcpdump, port mirroring
Start with flow records for the shape of the day. Move to full capture only to read what was said, and only with authority: packets hold personal data.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
21

## Slide 22
CHAPTER 5 · BASELINES, LOGS AND RESILIENCE
Baselines and Metrics
A baseline records bandwidth, latency, error rate and device load
Compare today against the baseline, not against a hunch
Threshold alerting simple to build, fires on fixed limits
Anomaly detection watches the shape of the data instead
Trending turns those records into a capacity forecast
Keep it honest a baseline is only valid until the network changes
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
22

## Slide 23
CHAPTER 5 · BASELINES, LOGS AND RESILIENCE
Logs and Integration
Log aggregation one searchable repository for every device
Syslog carries source, timestamp and message to a log server
Severity zero is emergency, seven is debug
A SIEM correlates across sources to find the pattern
Interfaces pull logs from cloud services into the same place
Automation can block a source or raise a case on one event
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
23

## Slide 24
CHAPTER 5 · BASELINES, LOGS AND RESILIENCE
Disaster Recovery Metrics
Metric | Question it answers | What it drives
Recovery Point Objective | How much data may we lose? | Backup frequency
Recovery Time Objective | How long may we be down? | Redundancy and failover
Mean Time To Repair | How fast do we restore service? | Repair process and spares
Mean Time Between Failures | How long before a failure? | Maintenance and refresh
Low numbers cost money. Agree them with the business, do not invent them.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
24

## Slide 25
CHAPTER 5 · BASELINES, LOGS AND RESILIENCE
Disaster Recovery Sites
Cold site space, power and connectivity, no equipment
Warm site some equipment in place, data not current
Hot site a live mirror: fastest recovery, highest cost
Distance far enough away to miss the same disaster
Latency close enough to keep replication workable
Regulation can decide where the data is allowed to sit
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
25

## Slide 26
CHAPTER 5 · BASELINES, LOGS AND RESILIENCE
High Availability Architectures
Active-active every node serves traffic and shares the load
Active-passive a standby waits for a heartbeat to stop
Load balancing spreads requests and steers away from dead nodes
Geographic redundancy survives the loss of a whole region
Stretched cluster spans two sites as a single cluster
The bill faster recovery always costs more capacity
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
26

## Slide 27
CHAPTER 5 · BASELINES, LOGS AND RESILIENCE
Disaster Recovery Testing
The rule a plan that has never been tested is unproven
Tabletop walk the plan through as a discussion
Simulation perform the recovery tasks away from production
Parallel test run recovery alongside live traffic
Full failover switch everything; the only complete proof
Afterwards document every test and repeat at least once a year
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
27

## Slide 28
BREAK
10 MINUTES
Back soon: the core services everything leans on, and the commands that verify them.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
28

## Slide 29
CHAPTER 6 · CORE SERVICES AND REMOTE ACCESS
Dynamic Addressing
The exchange discover, offer, request, acknowledge: recite DORA from memory
From nothing the client asks from no address at all, to the broadcast address
Relay agent carries the conversation to a server on another subnet
Reservation pins one address to one hardware address
Scope options deliver gateway, name servers and domain
Failover one server stands by, or both share the load
A client accepts the first offer it receives. That is the risk an attacker exploits.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
29

## Slide 30
CHAPTER 6 · CORE SERVICES AND REMOTE ACCESS
Automatic Addressing in Version Six
Method | Who assigns the address | Where it fits
Stateless autoconfiguration | The host, from the router advertisement | Simple networks, quick deployment
Stateful DHCPv6 | A server assigns and records it | Managed addressing, audit trail
Stateless DHCPv6 | Host assigns, server supplies options | Names and settings without addresses
Privacy extensions | Host rotates temporary addresses | Resists long-term tracking
The interface identifier can come from the hardware address, with FF FE inserted in the middle. Privacy extensions rotate it so a device cannot be tracked.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
30

## Slide 31
CHAPTER 6 · CORE SERVICES AND REMOTE ACCESS
Name Services
Root thirteen sets of root servers point each query down the hierarchy
Authoritative servers hold the records; resolvers ask on your behalf
Records A and AAAA, CNAME, MX, PTR and TXT
Time to live decides how long a resolver may cache an answer
Split horizon answers internal and external clients differently
DNSSEC signs records, so a forged answer fails validation
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
31

## Slide 32
CHAPTER 6 · CORE SERVICES AND REMOTE ACCESS
Time Synchronisation Services
Stratum zero the reference clock, atomic or satellite based
Stratum one servers connected directly to the reference
Lower strata spread the load away from the reference clocks
Use several sources for redundancy and cross checking
What drift breaks tickets, logs and incident timelines
Authenticate it so a forged source cannot move your clock
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
32

## Slide 33
CHAPTER 6 · CORE SERVICES AND REMOTE ACCESS
Virtual Private Networks
Site to site tunnel joins two offices over a public link
Remote access tunnel serves one user through client software
IPsec transport mode encrypts the payload only
IPsec tunnel mode encrypts the whole packet
Full tunnelling sends everything through the tunnel
Split tunnelling sends only corporate traffic through it
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
33

## Slide 34
CHAPTER 6 · CORE SERVICES AND REMOTE ACCESS
Remote Access and Device Management
Method | How it reaches the device | When to use it
Console cable | Direct serial connection, out of band | First setup, recovery, no network
Secure Shell | Encrypted command line over the network | Routine work and troubleshooting
Web interface | Browser session, usually encrypted | Simple tasks, less experienced staff
Programmatic interface | Application programming interface | Automation and scale
Every one of these paths is an attack surface. Harden all four, and turn off the ones you do not use.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
34

## Slide 35
KALI LINUX · VERIFICATION
Verifying services on Kali
DNS dig bbc.co.uk +short, cat /etc/resolv.conf
DHCP cat /var/lib/dhcp/dhclient.leases shows the lease history
Time ntpq -p, timedatectl, journalctl -u ntp
SSH ss -tnp | grep :22, grep sshd /var/log/auth.log
Services ss -tuln shows everything listening
The audit rule explain every listener or you have a gap
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
35

## Slide 36
KALI LINUX · VERIFICATION
Reading the evidence
Failed passwords grep 'Failed password' /var/log/auth.log | wc -l
Accepted logins grep Accepted /var/log/auth.log
Service ports in use ss -tunap | grep -E ':(22|53|123)'
The analyst habit correlate SSH and RDP times, users and flows
Log correlation one device shows an event; correlation shows the campaign
The red flag an unexpected listening port is an indicator of compromise
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
36

## Slide 37
QUIZ
Check your understanding
Open Quiz_Session_03.html in your browser.
20 questions, immediate feedback, topic tag on every question.
Read each explanation; the distractors teach as much as the answer.
Score 70%+ before moving on.
Every question maps to a session topic, e.g. 3A DNS.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
37

## Slide 38
KEY TAKEAWAYS
Ports come in pairs file transfer 21 and 22, Telnet 23 and SSH 22, web 80 and 443
Traffic is addressed four ways unicast, broadcast, multicast or anycast
Keep both diagrams current physical cabling and logical flow; a wrong drawing is worse than none
End of Support is the cliff patch with a rollback ready, and document the change
Recovery objectives choose the site and only a tested plan is real
Harden every management path console, command line, browser and interface
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
38

## Slide 39
REVISION CHECKLIST
Before next session
Learn the port pairs 21/22, 23/22, 25/587, 53, 67/68, 80/443, 161/162, 389/636, 5060/5061
Monitor with flows first keep flow records long; capture packets only when you must
Remember the core services dynamic addressing, names and time are what everything leans on
Run the commands dig, ss, ntpq and journalctl on any Linux box you can reach
Retake the quiz until you score 70%+ without guessing
Then take one habit forward before you change anything, ask what breaks if it fails
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
39

## Slide 40
NEXT SESSION
Session 4: Fundamental Security Concepts
The Security+ core begins: confidentiality, integrity and availability, the categories of control, and the frameworks that organise them
The CIA triad, non-repudiation and the AAA framework
Security controls by category and functional type
Zero trust, deception technology and change control
The NIST Cybersecurity Framework and gap analysis
Network Fundamentals + CompTIA Security+ SY0-701 · Session 3
© Billy Forrest
40