## Slide 1
TRAINING @ FORREST.ONE
SESSION 1 OF 12
Network Fundamentals + CompTIA Security+ SY0-701
Network Foundations: Networking Models & IP Addressing
How data moves across networks, from the signal on the wire to the subnet mask, and why every security control depends on it.
NETWORK
OSI/TCP-IP
SUBNETTING
© Billy Forrest

## Slide 2
WELCOME · THE JOURNEY
Twelve sessions, two strands, one goal
Strand | Sessions | Focus
Network foundation | 1–3 | Models, addressing, switching, services
Security+ core | 4–7 | Concepts, threats, crypto, IAM
Security architecture | 8–9 | Network, endpoint, application, cloud
Operations & governance | 10–12 | Vuln mgmt, IR, GRC
Why networks first, and how today is built
Six chapters: the language of networks, the OSI model, physical and data link, network and transport, media and topologies, then IPv4 addressing and subnetting. Every firewall rule and IDS signature speaks this language, and every attack travels over it.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
2

## Slide 3
SESSION OBJECTIVES
By the end of this session you will be able to
Seven OSI layers name each and its job
Encapsulation a header at every layer
Physical layer signals and media
MAC addressing 48-bit hardware addresses
TCP against UDP reliability or speed
Upper layers session, presentation, app
Wired and wireless choose suitable media
Topologies star against mesh
An IPv4 mask network against host
Subnets classless prefixes
Ten objectives, one quiz
The session quiz at the end of these three hours tests every objective on this slide.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
3

## Slide 4
CHAPTER 1 · THE LANGUAGE OF NETWORKS
Why layers matter at all
Troubleshooting without structure a user cannot reach a website, and you have no idea whether the fault is the cable, the switch, the route or the server
Seven layers, one job each every fault becomes findable because you can test the layers one at a time
Eliminate as you go test each layer in turn and rule it out
A map, not a product nobody sells you a layer five; the value is in the thinking
The whole value of the model
Split one impossible problem into seven small ones, and troubleshooting stops being guesswork.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
4

## Slide 5
CHAPTER 2 · THE OSI MODEL
The seven layers
Layer | Name | Role
7 | Application | The services users touch, such as web and email
6 | Presentation | Encoding, compression and encryption
5 | Session | Opens, manages and closes conversations
4 | Transport | Delivers end to end, uses port numbers
3 | Network | Logical addressing and routing
2 | Data Link | Delivers frames on a local segment
1 | Physical | Bits on the wire, light in fibre, radio waves
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
5

## Slide 6
CHAPTER 2 · THE OSI MODEL
The journey of a message
Layer | What it adds | Address used
7 to 5 · Application to Session | The data itself | None
4 · Transport | Segmentation and ports | Port number
3 · Network | Logical addressing | IP address
2 · Data Link | Local delivery | Hardware address
1 · Physical | Signals | None
The receiver reverses the process
Each layer peels one header off on the way up, until the application has the data it asked for.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
6

## Slide 7
CHAPTER 2 · THE OSI MODEL
Encapsulation: same data, different name
1
Data
from the application
2
Segment
transport adds ports
3
Packet
network adds IP addresses
4
Frame
data link adds hardware addresses
5
Bits
physical sends signals
Know the vocabulary precisely
TCP carries segments and UDP carries datagrams; both become packets at layer 3 and frames at layer 2.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
7

## Slide 8
CHAPTER 3 · PHYSICAL AND DATA LINK
The physical layer
Raw bitstream carried between devices, with no understanding of meaning at all
Three signal types electrical, light and radio
Copper electrical signals, using voltage changes for ones and zeros
Fibre light pulses, travelling further with far less interference
Wireless radio waves through the air, which buys you mobility
This layer defines standards cabling, connectors and signalling
First rule of troubleshooting
If layer one fails, nothing above it can possibly work. That is why the bottom of the stack is where you start.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
8

## Slide 9
CHAPTER 3 · PHYSICAL AND DATA LINK
Signals and their media
Signal | Medium | Notes
Electrical | Copper cable | Cheap and widely installed
Light | Fibre optic | Long distance, no interference
Radio | Air | Mobile, but shared airtime
Every medium is a trade
Cost, distance and interference. Those three factors will guide almost every cabling decision you make.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
9

## Slide 10
CHAPTER 3 · PHYSICAL AND DATA LINK
The data link layer
Node to node delivers data between devices on the same local network
Media Access Control 48 bits, written in hex, such as 00 1A 2B 3C 4D 5E
The frame the unit of data at this layer
Two sublayers Logical Link Control and Media Access Control
Error detection a Cyclic Redundancy Check appended to the frame
Assigned, not trusted set by the manufacturer, but changeable in software
Security note
Spoofing a hardware address is a software change, so layer 2 identity is never proof of identity.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
10

## Slide 11
CHAPTER 3 · PHYSICAL AND DATA LINK
The two data link sublayers
Sublayer | Responsibility | Faces
Logical Link Control | Identifies the layer 3 protocol, error checking | Up to Network
Media Access Control | Shares the medium, delivers by hardware address | Down to Physical
How the exam phrases it
Logical Link Control looks up towards the network layer; Media Access Control looks down towards the physical layer.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
11

## Slide 12
CHAPTER 3 · PHYSICAL AND DATA LINK
A dead link is almost always layer 1
The report a user has lost connectivity completely
The temptation dive into routing tables or firewall rules, because that feels clever
The discipline check the cable, the port indicator and the link state first
Why start low a dead link is usually physical, and physical faults are the most common and the cheapest to repair
Analyst's lens
Only once layer one is sound does it make sense to look higher up the stack.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
12

## Slide 13
CHAPTER 4 · NETWORK, TRANSPORT AND ABOVE
The network layer
Logical addressing IP addresses, as opposed to hardware addresses
Between networks it moves packets from one network to another
Routers the devices that operate at this layer
Time to Live drops by one at each router; at zero the packet is discarded
Multiple hops data crosses the internet one router at a time
Adapts to failure when a link fails, this layer chooses another path
The distinction that matters most
A hardware address identifies a device on a local segment. An IP address identifies a device across networks.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
13

## Slide 14
CHAPTER 4 · NETWORK, TRANSPORT AND ABOVE
The transport layer
Application to application delivers data end to end between applications
Port numbers so one machine runs web, mail and file sharing without confusion
Transmission Control Protocol connection oriented, numbers every segment, retransmits losses
User Datagram Protocol connectionless, no guarantee, no ordering, lower latency
The question to ask does this application need reliability, or does it need speed?
Where each one belongs
Reliability for web, email and file transfer, where a missing byte matters. Speed for voice, video and lookups.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
14

## Slide 15
CHAPTER 4 · NETWORK, TRANSPORT AND ABOVE
TCP versus UDP
Feature | Transmission Control Protocol | User Datagram Protocol
Connection | Connection oriented | Connectionless
Reliability | Guaranteed, retransmits | Best effort
Ordering | Sequence numbered | Not guaranteed
Speed | Slower | Faster
Typical use | Web, email, file transfer | Voice, video, lookups
Why latency beats retransmission
If a packet of a video call arrives too late you do not want it retransmitted. A missing byte of a file transfer, you do.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
15

## Slide 16
CHAPTER 4 · NETWORK, TRANSPORT AND ABOVE
The upper layers: 5, 6 and 7
Session establishes, manages and terminates conversations between applications
Session: dialogue control whose turn it is to talk, and checkpoints in long transfers
Presentation the translator, converting between data formats
Presentation: layer 6 handles compression and encryption
Application where HTTP for the web and DNS for name resolution live
Exam trap
The application layer is the protocol layer, not the program itself. That distinction is examined directly.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
16

## Slide 17
DISCUSSION
Name the layer first, then the control presents itself. Why does that work?
A web attack arrives at layer 7, so the answer is a web application firewall. A spoofed packet arrives at layer 3, so filter at the router. A rogue switch or a poisoned address table is layer 2, so use port security.
Each layer has its own attack and its own defence, and that is a direct consequence of each layer having one job.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
17

## Slide 18
BREAK
10 MINUTES
Back soon: the media your signals travel through, the topologies we arrange them in, then IPv4 addressing and subnetting.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
18

## Slide 19
CHAPTER 5 · MEDIA AND TOPOLOGIES
Wireless transmission media
Radio waves carry data through the air, with no cabling to install
Mobility the obvious benefit of the wireless medium
Frequency bands the band you choose is a real trade-off
Lower frequencies travel further, pass through walls, carry less data
Higher frequencies carry much more data over shorter distances
The limitation wireless is shared, so every device competes for airtime
Design note
Performance drops as clients join the channel, and drops further with outside interference.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
19

## Slide 20
CHAPTER 5 · MEDIA AND TOPOLOGIES
Wired transmission media
Twisted pair the cheapest and easiest to install, so it fills every office
Categories rate capability, such as Category 5e and Category 6
Shielding reduces interference from motors, lighting and other sources
Coaxial higher frequencies than twisted pair; legacy networks and broadband
Fibre carries light rather than electricity, so it is immune to interference
Fibre distance spans the longest distances at the highest bandwidth
Rule of thumb
Running a link between two buildings? Fibre is almost always the answer.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
20

## Slide 21
CHAPTER 5 · MEDIA AND TOPOLOGIES
Choosing the right cable
Media | Signal | Best for
Twisted pair | Electrical | Office desktops, short runs
Shielded twisted pair | Electrical | Electrically noisy areas
Coaxial | Electrical | Legacy networks, broadband
Fibre optic | Light | Long distance, high bandwidth
Three questions choose the cable
How far? How much bandwidth? How much interference? Distance, bandwidth and interference decide.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
21

## Slide 22
CHAPTER 5 · MEDIA AND TOPOLOGIES
Connectors and transceivers
Transceiver converts between signal types, so a copper port can talk to fibre
Registered Jack 45 the standard copper connector, on almost every desktop
Fibre connectors Subscriber Connector and Lucent Connector
Small Form factor Pluggable hot swappable, so media type changes without downtime
Media converters bridge a copper segment to a fibre segment
A design decision connector choice affects maintenance, not just speed
Why hot-swappable matters
You can change the media type on one port without taking the switch out of service.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
22

## Slide 23
CHAPTER 5 · MEDIA AND TOPOLOGIES
Star, mesh and hybrid
Star every device connects to a central point, usually a switch
Star benefit easy to troubleshoot, because each device has its own cable
Star weakness the central point is a single point of failure
Full mesh links every node to every other node, so any link can fail
Mesh trade maximum resilience at maximum cost and complexity
Hybrid meshes what needs resilience and stars the rest
One question, every topology
How much will you spend to survive a failure?
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
23

## Slide 24
CHAPTER 5 · MEDIA AND TOPOLOGIES
Star against mesh
Topology | Strength | Weakness
Star | Simple: one fault, one device | Central point can fail
Full mesh | No single point of failure | Expensive and complex
Hybrid | Resilience where it matters | Needs careful design
Spine and leaf | Predictable latency | Requires more links
Spine and leaf, the data centre pattern
Every leaf switch connects to every spine switch, so any two devices sit the same number of hops apart.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
24

## Slide 25
CHAPTER 6 · IPV4 ADDRESSING AND SUBNETTING
IPv4 address fundamentals
32 bits split into four groups of eight, and each group is an octet
Dotted decimal 192.168.1.1, because the machine sees 32 binary digits
Each octet runs from 0 to 255
The whole space about 4.29 billion addresses
Why subnetting exists nobody expected to run out of that space
Reserved ranges withheld from public use, so private ranges are reusable
Start here every time
Thirty two bits, four octets, dotted decimal. Know the structure before you touch a mask.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
25

## Slide 26
CHAPTER 6 · IPV4 ADDRESSING AND SUBNETTING
Addresses to recognise on sight
Range | Purpose | Note
10.0.0.0/8 | Private | Reusable inside any organisation
172.16.0.0/12 | Private | Not routable on the public internet
192.168.0.0/16 | Private | The common home and office range
127.0.0.1 | Loopback | Always means the local machine
169.254.0.0/16 | Automatic | Self-assigned when no server answers
A symptom, not a configuration
A 169.254 address means the machine asked for an address and nothing answered. Investigate the failure, not the address.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
26

## Slide 27
CHAPTER 6 · IPV4 ADDRESSING AND SUBNETTING
Subnet masks
A mask is 32 bits a run of ones followed by a run of zeros
The ones mark the network portion
The zeros mark the host portion
255.255.255.0 means the first three octets are the network
Two addresses are reserved the lowest is the network, the highest is the broadcast
Subnetting divides one network into smaller segments
Count carefully here
Eight host bits give 256 values, minus the network and the broadcast: 254 usable hosts, in every subnet.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
27

## Slide 28
CHAPTER 6 · IPV4 ADDRESSING AND SUBNETTING
Worked example: reading a subnet mask
1
The address
192.168.1.50
2
The mask
255.255.255.0
3
The network
192.168.1.0
4
The host range
192.168.1.1 to .254
5
The broadcast
192.168.1.255
The pattern never changes
Find the network, count up from one, and stop one short of the broadcast. Do that quickly and you have the foundation.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
28

## Slide 29
CHAPTER 6 · IPV4 ADDRESSING AND SUBNETTING
Classless addressing
Classless Inter-Domain Routing replaced the rigid class system
The slash states how many bits are the network
/24 equals the mask 255.255.255.0
Counter-intuitive a larger slash number means a smaller network
/30 gives just two addresses, which is why it links two routers
Variable Length Subnet Masking lets each subnet differ in size, largest first
Why classless won
Classful addressing wasted whole blocks. CIDR lets the boundary fall at any bit, so the space you have is the space you use.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
29

## Slide 30
CHAPTER 6 · IPV4 ADDRESSING AND SUBNETTING
Prefix notation at a glance
Prefix | Subnet mask | Usable hosts
/24 | 255.255.255.0 | 254
/25 | 255.255.255.128 | 126
/26 | 255.255.255.192 | 62
/27 | 255.255.255.224 | 30
/30 | 255.255.255.252 | 2
The pattern to remember
Every extra prefix bit halves the addresses available, and two are always lost to the network and the broadcast.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
30

## Slide 31
QUIZ
Activity: quick subnet arithmetic
What is the network address of 192.168.10.50/28?
How many usable hosts in a /29 subnet?
What is the CIDR notation for mask 255.255.255.240?
Borrow 2 bits from a /24: how many subnets of what size?
Which address can never be assigned to a host?
Block size shortcut: for /28 the block is 16, so 50 falls in the .48 to .63 range.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
31

## Slide 32
QUIZ
Check your understanding
Open Quiz_Session_01.html in your browser.
20 questions, immediate feedback, and a topic tag on every question.
Read each explanation: the distractors teach as much as the answer.
Score 70% or better before moving on.
Every question maps to a session topic area, for example 1B IPv4 Addressing.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
32

## Slide 33
KEY TAKEAWAYS
Seven layers, one job each which is what makes every fault findable by testing one layer at a time.
Encapsulation changes the name data, segment, packet, frame, then bits on the medium.
Layer 2 is local 48-bit hardware addresses deliver frames on one segment.
Layer 3 routes IP addresses carry packets between networks, and Time to Live stops loops.
TCP guarantees, UDP is fast choose reliability or latency for the application.
Media is a trade distance, bandwidth and interference choose the cable.
Topology trades cost for resilience decide where you can afford to fail.
The mask splits network from host so a /24 gives 254 usable hosts, not 256.
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
33

## Slide 34
REVISION CHECKLIST
Before next session
Retake the quiz until you score 70% or better without guessing
Practise subnetting ten /24 to /30 calculations by hand
Walk the stack name each layer, its job and one protocol, out loud
Choose three cables justify each with distance, bandwidth and interference
Read ahead Session 2: switching, VLANs and spanning tree
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
34

## Slide 35
NEXT SESSION
Session 2 — Switching, VLANs & Network Architectures
Layer 2 forwarding, virtual LANs and the topologies that segment a campus
MAC addresses and the switch forwarding table
VLANs, trunking and 802.1Q tagging
Spanning Tree Protocol and loop prevention
Network Fundamentals + CompTIA Security+ SY0-701 · Session 1
© Billy Forrest
35